Open source tools for logic synthesis and SOC Design: An overview
Varun Mohan
Mtech Embedded Systems
National Institute of Electronics And IT

---
About me
About me
- CS graduate
- Currently pursuing Mtech in embedded system @ NIELIT Calicut.
- Passionate About RTL|Digital Design and FPGA based systems and accelerators.
- Other fields of interest
  - Bare Metal C Programming | HW/SW CO Design | Computer Architecture

---
This talk is not about
This talk is not about
- RTL Design
- Verilog
- Verification

---
Expectations from you
Expectations from you
- Basic Digital Design knowledge
- Basics of verilog
- Basics of writing testbenches
- Using Linux command line

---
Agenda
Agenda
Open source tools for logic synthesis
  - Functional verification of digital design
  - Synthesis and Mapping
  - Gate Level Simulation
  - Demo : Generating bitstream for an FPGA using a open source flow
- Litex
  - How to install litex
  - How to run your first simulation with microwatt with litex.

---
Functional Verification
Functional Verification
Simulation
  - Simulation is the process of checking whether the design is adhering to the given specs. The tool used for simulating the design is called a simulator.
- Inputs to the simulator
  - The Design.
  - The Testbench.
- Tool Used
  - iverilog

---
Functional Verification - iverilog flow
Functional Verification - iverilog flow

---
Logic Synthesis - What is it.?
Logic Synthesis - What is it.?

---
Logic Synthesis - Translation
Logic Synthesis - Translation

---
Logic Synthesis - Optimisations
Logic Synthesis - Optimisations

---
Logic Synthesis - Mapping
Logic Synthesis - Mapping
The standard cell library
  - A standard cell library is a collection of characterized logic gates that can be used to implement digital circuits. This is usually part of set of file created by the foundry called the PDK(Process Development Kit).
  - Has many type of files including the timing/power liberty file.
  - The SkyWater Open Source PDK
    - The SkyWater Open Source PDK is a collaboration between Google and SkyWater Technology Foundry to provide a fully open source Process Design Kit and related resources, which can be used to create manufacturable designs at SkyWater’s facility.

---
Gate Level Simulation
Gate Level Simulation
Why GLS
  - check the correctness of the design after synthesis
- Synthesis Simulations Mismatches
  - Missing signals in sensitivity list
  - Blocking and Nonblocking statements
  - Missing statements in if|case blocks

---
GLS with iverilog
GLS with iverilog

---
Demo
Demo

---
Installing yosys
Installing yosys
- mkdir /tmp/yosys
- cd /tmp/yosys
- sudo apt install build-essential clang bison flex libreadline-dev gawk tcl-dev libffi-dev git graphviz xdot pkg-config python3 libboost-system-dev libboost-python-dev libboost-filesystem-dev zlib1g-dev
- git clone https://github.com/YosysHQ/yosys.git
- cd yosys
- make clean
- make config-gcc
- make
- sudo make install

---
Installing iverilog and gtkwave
Installing iverilog and gtkwave
- sudo apt install iverilog
- sudo apt install gtkwave

---
Litex
Litex
- A Framework that provides a convenient and efficient infrastructure to create FPGA Cores/SoCs
- Migen
- Buses including Wishbone and AXI
- Easy to integrate VHDL/Verilog/SystemVerilog code in LiteX!
- LiteX already supports various softcores CPUs including microwatt!!

---
Typical LiteX design flow
Typical LiteX design flow

---
Demo - Simulating a microwatt  based SOC with Litex
Demo - Simulating a microwatt based SOC with Litex